## Slide 1: SystemC Multi-language requirements
Accellera Multi-Language Verification Working Group

## Slide 2: Outline
Introduction
Multi-language Verification Working Group
Requirements
Implementation proposal
Next steps
2

## Slide 3: Introduction
SystemC is more and more used in advanced verification frameworks to act as test bench or Verification IP (VIP)
In verification, test bench and VIP construction and elaboration happens separately and independently from the design module hierarchy
In a multi-language environment, the creation and instantiation of SystemC verification components or subtrees is often initiated from other verification languages/frameworks (e.g. UVM)
Enhancements to the SystemC standard and language are expected to support its application in multi-language verification frameworks
3

## Slide 4: Multi-language Verification WG
Chair: Warren Stapleton (AMD)
Vice Chair: Faris Khundakjie (Intel)
The mission of the MLVWG is to create a standard and functional reference for interoperability of multi-language verification environments and components.
The MLVWG have reviewed requirements and are developing an open source proof-of-concept library for creating a standards-based approach for combining verification environments developed in different languages/frameworks.
In addition, the group will look at ways to enable the introduction of UVM (Universal Verification Methodology) concepts in other environments and languages that come from legacy projects or developed with other frameworks for beneficial reasons
4

## Slide 5: MLVWG – Architecture
5

## Slide 6: Requirements related to UVM-SV  SystemC interoperability
Allow instantiation of SystemC modules acting as testbench/VIP component after start of simulation, e.g. introducing dedicated “testbench elaboration” callback(s)
These additional “testbench elaboration” callbacks should not be called by the SystemC module registry, but by the application (e.g. UVM environment)
For proper time synchronization between SystemC and the external verification environment, sc_start(<time>) should stop at the first delta of the time in question, not before
Introduce a dedicated function to start a test (similar to UVM run_test), including the invocation of the “testbench elaboration” callback(s), UVM phasing and ML time synchronization
6

## Slide 7: Implementation proposal
Introducing “quasi-static elaboration”
Introducing multi-language-enabled time synchronization
NOTE: The syntax and naming applied for the implementation is just an initial proposal. Definitive syntax and naming is considered part of the alignment discussion and prototyping exercise
7

## Slide 8: Quasi-static elaboration
Introducting “testbench elaboration” specific callback(s)
  quasi_static_end_of_construction
  quasi_static_end_of_elaboration
  quasi_static_complete_binding
  quasi_static_start_of_simulation (which also closes the quasi-static stage)
All methods are public
These callbacks are not called by the SystemC kernel, but by an application (e.g. UVM)
When quasi_static_start_of_simulation callback is invoked (e.g., by the UVM phase engine), it merges the new registries into the old ones, places the old ones into their places and deletes the new ones.
8

## Slide 9: ML-enabled time synchronization
Problem: sc_start(<time>) causes the SystemC kernel to stop just before the first delta of the specified time, rather than entering it.
Implementation options
  Introduce new method sc_simcontext::co_simulate(<time>) which actually enters the first delta of the specified time.
  sc_simcontext::simulate(<time>, <flag>) if <flag> is enabled, the simulation steps after entering the first delta of the specified time, otherwise the default behavior is maintained.
9

## Slide 10: Next steps
Discussion in MLVWG and LWG on requirements and technical feasibility
Explore standardization and implementation opportunities
  SystemC standard API update (incorporate in upcoming IEEE 1666 cycle?)
  Update Accellera SystemC PoC
Discuss topic at Accellera’s SystemC Evolution Day 2018
  Talk/abstract submission under development
Inform Technical Committee and TC Chair on this X-WG initiative
10

## Slide 11: Acknowledgment
Alex Chudnovsky, Vitaly Yankelevich - Cadence
Bryan Sniderman, Warren Stapleton - AMD
Faris Khundakjie – Intel
11

## Slide 12: Interesting links
MLVWG public page http://www.accellera.org/activities/working-groups/multi-language
MLVWG Accellera working area http://workspace.accellera.org/apps/org/workgroup/mlwg/
MLVWG at github https://github.com/OSCI-WG/Multi-Language
12