## Slide 1: TLM-Serial Status and future work
Jerome Cornet - ST
Ingo Feldner – Robert Bosch GmbH

## Slide 2: Presentation Copyright Permission
  A non-exclusive, irrevocable, royalty-free copyright permission is granted by Robert Bosch GmbH to use this material in developing all future revisions and editions of the resulting draft and approved Accellera Systems Initiative SystemC standard, and in derivative works based on this standard.

## Slide 3: TLM-serial: The Past
Problem Statement
Electronic Control Units (ECUs) rely on serial on/off-chip interfaces to connect to IP and ECU networks Assembling virtual ECUs can introduce high effort due to proprietary abstract serial interface implementations
Goal
Establish modeling standard for serial on/off ECU interfaces to enable quick and easy assembly of VPs
IFX
FSL
REL
RB
ST
RB
SPI
IFX
FSL
REL
RB
ST
RB
SystemC-TLM2
SPI
Abstraction

## Slide 4: TLM-serial: The Past
Why a new serial standard?
  Defined scenarios and use-cases
    Based on identified industry needs and real-world problems
  CAN, SPI, I2C taken as starting points
    As most experience by parties and concrete need
  Implemented and proven with prototypes and examples
  Definition of rules per serial protocol
  Key elements:
    Simplicity
    Connection to RTL
    Definition of Corner Cases (e.g. reset)

## Slide 5: TLM-serial: The Present
Dedicated implementations per serial protocol
  Each protocol needs dedicated rules
  Implementation is re-used where possible
Ready-to-use TLM-CAN protocol and implementation of TLM-CAN(-FD) available
  Supports all defined CAN scenarios shared here: https://workspace.accellera.org/apps/org/workgroup/tlmwg/download.php/14231/SerialTLM_requirements_and_scenarios.doc
  Donated to Accellera and available to members at: https://github.com/OSCI-WG/tlm-serial/tree/master/tlm-can Implementation can be shared with interested parties
Working prototypes for TLM-SPI and TLM-I2C

## Slide 6: TLM-serial: The Future
Bosch will demand TLM-CAN from suppliers
  Own models already prepared
Continue work in 2019
  Finalize SPI and I2C
  New protocol candidates: LIN, SENT, MSC
  Workshop for discussing scenarios and collaboration in spring 2019
Looking for contributors
  With relevant scenario and business need
  From different domains
  INTERESTED? PLEASE CONTACT US AND DISCUSS WITH US!