## Slide 1: SystemC AMS Update
Karsten Einwich

## Slide 2: Presentation Copyright Permission
  A non-exclusive, irrevocable, royalty-free copyright permission is granted by COSEDA Technologies GmbH to use this material in developing all future revisions and editions of the resulting draft and approved Accellera Systems Initiative SystemC standard, and in derivative works based on this standard.

## Slide 3: SystemC AMS update
SystemC AMS Update
  Generalized AC
  Piece wise linear
  Interactive tracing
  Physical domains
Future thoughts
Agenda

## Slide 4: SystemC AMS update
Provide AC-Implementation for SC-modules (e.g. implemented digital filter)
Provide AC-implementation for hierarchical models, which can not be modelled as composed submodules (e.g. SD-converter)
Cross boundaries – e.g. bussystems for AC-simulation
Generalized AC - Motivation

## Slide 5: SystemC AMS AC Modeling
AC-analysis:
  Calculates linear complex equation system stimulated by AC-sources
  -> Linear frequency dependent transfer function (bode diagram)
AC noise domain
  solves the linear complex equation system for each noise source contribution (other source contributions will be neglected)
  adds the results arithmetically
ELN and LSF description are specified in the frequency domain
TDF description must specify the linear complex transfer function of the module inside the callback method ac_processing (otherwise the out values are assumed zero)
  This transfer function can depend on the current time domain state (e.g. the setting of a control signal)
Small Signal Frequency Domain Analysis (AC-Analysis)

## Slide 6: SystemC AMS AC Modeling
Linear equation system contribution for LSF/ELN:
Small-Signal Frequency-Domain Analysis for ELN, LSF and TDF
LSF model
ELN model
TDF model
Complex linear equation system
Sources
TDF
LSF
LSF
TDF
vp,n
eln_module
lsf_module
k
d
dt
R1
C1
H(s)
H(z)
tdf_module
AC
AC

## Slide 7: SystemC AMS AC Modeling
SCA_TDF_MODULE(combfilter)
{
sca_tdf::sca_in<bool> in;
sca_tdf::sca_out<sc_int<28> > out;
void set_attributes()
{
in.set_rate(64); // 16 MHz
out.set_rate(1); // 256 kHz
}
void ac_processing()
{
double k = 64.0;
double n = 3.0;
// complex transfer function:
sca_complex h;
h = pow( (1.0 – sca_ac_z(-k)) /
(1.0 – sca_ac_z(-1)),n);
sca_ac(out) = h * sca_ac(in) ;
}
Frequency Domain Description for TDF Models
void processing()
{
int x, y, i;
for (i=0; i<64; ++i) {
x = in.read(i);
…
out.write(y);
}
SCA_CTOR(combfilter)
{
…
}
};

## Slide 8: Generalized AC
Motivation
Weinan Tang and Weimin Wang
“A single-board NMR spectrometer based on a software defined radio architecture”

## Slide 9: Generalized AC
Each SC-module can be derived from a sca_ac_module base class
This base class has a pure virtual method for providing the ac transfer function
Each sc_core::sc_port_base connected to a sc_core::sc_interface can be accessed via sca_ac_analysis::sca_ac and thus used as an AC-in or outport
All AC-modules instantiated as childs (lower in hierarchy) of an sca_ac_module are ignored
Concept

## Slide 10: Generalized AC
class sca_ac_object
{
public:
void ac_enable();
void ac_disable();
bool is_ac_enabled();
sca_ac_object();
virtual ~sca_ac_object();
};
class sca_ac_module : public sca_ac_object
{
public:
virtual void ac_processing()=0;
protected:
virtual ~sca_ac_module(){}
};
template<class T>
sca_complex& sca_ac(const sc_core::sc_out<T>&);
template<class T>
const sca_complex& sca_ac(const sc_core::sc_in<T>&);
Current Implementation
Base class provides some “gimmick” methods – to activate deactivate the ac module during elaboration
Base class used to provide the ac-implementation
Port access functions

## Slide 11: Generalized AC
SC_MODULE( mod_lp ), sca_ac_analysis::sca_ac_module
{
sc_core::sc_in<int> inp; // input port
sc_core::sc_out<int> outp; // output port
void ac_processing()
{
sca_util::sca_complex in = sca_ac_analysis::sca_ac(inp);
sca_ac_analysis::sca_ac(outp) = sca_ac_analysis::sca_ac_ltf_nd(num,den,in);
}
SC_CTOR(mod_lp)
{
num(0)=1.0;
den(0)=1.0;
den(1)=1.0/(2.0*M_PI*1e3);
}
private:
sca_util::sca_vector<double> num, den;
};
Example

## Slide 12: Piece Wise Linear
Extension to SystemC AMS ELN and LSF
Permits modelling of non-linear behavior by a piece wise linear approximation
Especially efficient for switched circuits
  PWM, DCDC-converter, …
Motivation

## Slide 13: Piece Wise Linear
The SystemC AMS standard defines linear elements for electrical networks and signal flow only
The COSIDE piece wise linear models permit the use of approximated non-linear elements without a significant influence on the solver performance and robustness in case of abstract models
Well suited for non-linear circuits, which have different linear working points (e.g. switched networks with diodes)
For ELN we provide an additional double vector parameter pwl_value for all controlled sources (sca_cccs, sca_ccvs, sca_vccs, sca_vcvs) and for LSF we provide this additional parameter for sca_lsf::sca_gain
  If the vector is not empty (otherwise the original scalar parameter value is used) it will be interpreted as piece wise linear characteristic – input-output value pairs
For ELN we provide piece wise constant voltage controlled resistor and capacitor
SCA PWL Libraries – Principle

## Slide 14: Piece Wise Linear
The vector represents value pairs – vector size (number of pairs) must be at least 2
Before the first and after the last point the segment will be continued
The solver will not skip segments – the solver reduces internally the step width
sca_eln::sca_cccs, sca_eln::sca_ccvs, sca_eln::sca_vccs, sca_eln::sca_vcvs, sca_lsf::sca_gain
PWL Vector Definition
x
x
x
x
in
out
1
-1
-2
2
3
4
5
2
1
pwl_value=sca_create_pair_vector(-2.0,-0.6, -1.0,-0.4, 1.0,0.4, 2.0,5.0) pwl_value={ {-2.0,-0.6} , {-1.0,-0.4}, {1.0,0.4}, {2.0,5.0} } //C++11
-1
-2

## Slide 15: Piece Wise Linear
PWC (piece wise constant) Vector Definition
The vector represents value pairs – the vector must contain at least one pair
Before the first and after the last point the segment will be continued
The solver will not skip segments – the solver reduces internally the step width
sca_eln::sca_vcc (voltage controlled capacitor), sca_eln::sca_vcr (voltage controlled resistor)
pwc_value = sca_create_pair_vector(-2.0,-2.0, -1.0,-0.4, 1.0,0.4, 2.0,5.0)
pwc_value = { {-2.0,-2.0}, {-1.0,-0.4}, {1.0,0.4}, {2.0,5.0} } //C++11

## Slide 16: Piece Wise Linear
PWL modelling example – simple diode
-2
x
x
x
V(V)
I(A)
1/ron
vth
vth+1
vth/roff

## Slide 17: Interactive Debug Feature / Extendable and unified Tracing
Enabling Interactive feature of Cadence Incisive for SystemC AMS
  Cooperation: NXP-Cadence-COSEDA
  -> vendor independent interface for SystemC AMS defined
  Can/Should be generalized for SystemC ?
Motivation / History

## Slide 18: Interactive Debug Feature / Extendable and unifed Tracing
Getting current (at SystemC time) value of ELN nodes, TDF and LSF signals, current traceable ELN modules and TDF trace variable
  As string (using >> operator)
  As object of the corresponding type
Callback if a new value is available
Force / release values for TDF signals (ELN/LSF would structural change the equation system)
(Deposit value)
Feature

## Slide 19: Interactive Debug Feature
virtual bool register_trace_callback(sca_trace_callback, void*);
  typedef void (*sca_trace_callback)(void*);
  Registers callback, which is executed if a new value has been produced, returns false if the corresponding object does not support tracing – the callback is called with the given void pointer as argument
virtual const std::string& get_trace_value() const;
  Returns the current value (as string) of the object at the current SystemC time (sc_core::sc_time_stamp())
  Returns an empty string, if the object does not support tracing e.g. the signal is non-causal
Interface in sca_traceable_object 1/2

## Slide 20: Interactive Debug Feature
virtual bool force_value(const std::string&);
  Forces the signal with the value given by the string, the value becomes valid with the start of the next cluster period, the force only influences the read’s form the signal – the written and thus traced value remains
  Returns false, if the value cannot be forced (the string cannot be converted or the object does not support value forcing like electrical elements)
virtual void release_value();
  Releases a forced value, the value is released with the start of the next cluster period
Interface in sca_traceable_object 2/2
May also useful for SystemC signals

## Slide 21: Interactive Debug Feature
const T& get_typed_trace_value() const;
  Returns the current value of the object at the current SystemC time (sc_core::sc_time_stamp())
  Will be used by const std::string get_trace_value()
void force_typed_value(const T&);
  Forces the signal with the value, the value becomes valid with the start of the next cluster period, the force only influences the read’s form the signal – the written and thus traced value remains
  The method is used by void force_value(const std::string&)
Additional methods for sca_tdf::sca_signal<T> + ports

## Slide 22: SystemC AMS Physical domain Modelling
Modelling the environment of integrated systems
Running application scenarios
Executable specification
Motivation

## Slide 23: SystemC AMS Physical domain Modelling
Physical domains can be modelled using the available SystemC / SystemC AMS classes
Physical domain libraries can be generated by derivation using analogy relations
If required you can build on top of SystemC/SystemC AMS unit systems (e.g. using the newest C++ feature)
-> Missing: debug/tracing cannot recognize the units
Requirements

## Slide 24: SystemC AMS Physical domain Modelling
Discussion whether property annotation is sufficient
  String properties for:
    domain
    Unit
Virtual sc(a)_interface function (default implementation – empty string
Discussion

## Slide 25: Future thought
Can we do more generalization?
  E.g. enable customized static analyzes (budget (level, noise, nonlinearity, …) analysis, power, …)
    Missing exploration capabilities – e.g. which port is connected to a port, which ports are connected to an interface, …
  Combine TDF / SystemC on primitive level -> easier TLM->TDF interaction
  Allow direct connection ELN<->LSF